PI Firmware
Commands/Queries

demo software commands
May 5, 2020

Table of Contents

# PI FIRMWARE
## Source Repository, Compiling, and Executable
The source code has all been written in C, for speed of execution and compatibility with the GPIO library used on the pi (bcm2835). The github repo where the source code can be accessed is:
https://github.com/johnpolakow/PI_Blackbox
The directory for code executing on the pi is “PI_Firmware”. To get a sample client application, which already works with the pi firmware, look in the “Client_Code” folder.
For compiling the firmware on the pi, here is the command (make sure bcm2835 library has been installed if this is a fresh OS):
gcc -g -o exec Execution_Engine.c -l pthread -l bcm2835 -l m
If debugging capabilities are desired use this command:
gcc -g -fsanitize=address -static-libasan -o exec Execution_Engine.c -l pthread -l bcm2835 -l m
The client code is easy to compile:
gcc -o client client.c
IF EXECUTING MANUALLY, MUST EXECUTE PROGRAM WITH SUDO
Note: the binary executable for the program must be executed on the raspberry pi with the “sudo” command. The pi requires programs which access the GPIO pins to have elevated access. If sudo is not used there will be a segmentation fault.
sudo ./exec
Note2: By default the pi has been configured to automatically start execution of the program at boot, MANUAL EXECUTION IS NOT NECESSARY. Under normal circumstances it is not necessary to execute the program manually. If you desire to for testing or debug purposes, make sure to preface the command with sudo.
## Metrics Captured
The metrics directly measured by the Pi Blackbox are:
- Power delivered to the Cooler Driver Board (Volts, mA, Watts)
- Dewar Temp Diode Voltage, and associated LUT temperature (Volts, Kelvins)
- Power delivered to heat load resistor in the Dewar (V, mA, mW)
- Heat Load State (On/Off)
- Relay State for Cooler Driver (On/Off)
- Temperature of x3 attached K-type thermocouples (Celsius)

## Capture Rate(s)
Each metric once per second. Every second a complete iteration of the various metrics are read and saved to storage. The pi can be queried over the socket interface as often as necessary to retrieve the metrics. If querying more than once per second, examine the timestamp in the metrics readout to ascertain whether a duplicate read has been sent. The pi responds with whatever the latest data is.

The Pi firmware captures each metric sequentially, then writes the data points to file. Each datalog point of the above metrics is paired with:
- Timestamp ( MM/DD/YYYY hh:mm:ss )
- Elapsed Running Time when sample taken

# Software Specification
## Timestamp, Date-Time Naming Convention
A timestamp shall be represented in the format:
[MM-dd-YYYY]_[hh.mm.ss]

MM	2 digit month
dd	2 digit day of month
YYYY	4 digit year
hh	2 digit hour
mm	2 digit minute
ss	2 digit second

* 2 digit refers to the convention of including a leading zero if the value	is less than ten.
** To avoid AM/PM confusion, the two digit hour shall be in the 24 hour	based format. For example the hour 6:01:35 PM is represented as	18:01:35

Example:
Timestamp for Jan. 27th 2020 @ 3:18:34 PM is- 01/27/2020_15.18.34

## Log File

### Log File Structure
// filename: XXXXXX
## PI_BB LOG FILE ##
firmware version XXXXX, PCB version
PI_BB: [blackbox#]
CCC:	CCC_ID
Compressor:	Compressor_ID
Dewar:	Dewar_ID
Displacer:	Displacer_ID
Test Execution:	[Manual] or [profile filename]
Test_Type:	[default/Performance/Lifetime/BurnIn]
Log Start:	[Timestamp]

[COLUMN LEGEND]
_______________________________________________________________
DATA	[TIMESTAMP]
COMMAND	[TIMESTAMP]
DATA	[TIMESTAMP]
STOP	[TIMESTAMP]
________________________________________________________________

To avoid confusion and misinterpretation, the units of measure are included in both the Legend and immediately following the value of each metric. For instance a voltage is recorded as:
12.013V
### Log File Path
If a USB drive is inserted, the Linux kernel has been configured to mount it to:
/home/pi/USB_drive/
The flash drive is the default storage device if present. The Log file path is then:
/home/pi/USB_drive/Logs/filename.log
If a USB flash drive is not detected, the micro SD card will be used to store the data, and the path will be:
/home/pi/Logs/filename.log
The log file is automatically created and stored when the “>start_test” command is issued.
Note: When configuring the software to auto-launch at boot, it broke the save to USB functionality, so all Logs are being stored on the pi at:
/home/pi/Logs/filename.log
USB save functionality will be restored in the next software release.
### Log File Upload
Currently the log file upload to hub is not implemented. The logs can be accessed manually however.
# Socket Interface Specification
## Socket Instantiation
The socket hosted on the pi opens and listens on port 2020, waiting for any client to connect. The client can connect to the pi over Ethernet or Wifi, it is interface agnostic. The Pi listens on port 2020 for any incoming connection. The pi waits for clients to connect to it, the pi does not initiate any connections. The socket is configured as TCP/IP protocol, with the following socket parameters:
.ai_family = AF_INET;
.ai_socktype = SOCK_STREAM;
.ai_flags = AI_PASSIVE;

A sample client program has been written and is included to illustrate how to use the interface. The pi will always send a response to any client instruction.
## Socket Command Structure
All “commands” or instructions will originate from the hub computer. There are two types of instructions sent to a PI_BB:
- Get Instruction– will refer to as a ‘Query’
- Set Instruction – referred to as a ‘Command’
Query Instructions must begin with a ‘?’.
Command Instructions must begin with a ‘>’.
If an instruction is sent without the proper prefix of ‘?’ or ‘>’, or there is a typo in the instruction, the parser responds with an error message.

The commands/queries are not case sensitive, even though the commands are shown as all capital letters in this document.
## Query List
Not all queries are implemented yet. The non functional queries are greyed out.
?status	Return the following parameters:
hostname
eth0 IP address
wlan0 address
flash drive disk usage
SD card disk usage
DUT ID for:
compressor
DDCA
displacer
CCC
Pi CPU temperature
Test status (whether executing a test or not)
Execution set to manual or profile
Current time & date on PI

?profiles	list the profiles currently stored on SD card

?logs	list the logs currently stored on SD card
?profile	list the current selected profile, if any
?show [filename]	print the contents of the file. Could be a profile, log, config	file, etc.

?metrics	Returns a snapshot of the current measurements.

?time	Current date-time PI thinks it it right now

?	If no argument is supplied with the query instruction, the list of	query instructions is printed

help	Prints query instructions and command instructions with	usage info. Note this command does not require a ‘?’ or ‘>’.

## Command List
DEBUG [ON/OFF]	Turn additional debug information on or off. This may help	when writing software to interface with the pi. Note the	“>” character is not used to prepend the command with.

VERBOSE [ON/OFF]	Turn verbose responses on or off. Verbose	responses include the column headers for the metrics	command. Note the “>” character is not used to prepend	the command with.

>START_TEST	Starts test execution, within the confines of selected	test parameters. At present, because profile functionality is	not complete yet, the >start_test command only causes the	log file to begin recording.

>RELAY_ON	Turn on the relay.

>RELAY_OFF	Turn off the relay.

>SET_LOAD	[value]	Set the load resistor power dissipation in milliWatts.	The load is not turned on with this command, just set	to the value of the supplied argument. When the	LOAD_ON command is issued, then power will be	applied at the load dissipation value supplied in this	command.

>LOAD_ON	Set the load resistor current to the value prescribed by the	SET_LOAD command. Default load current is 0 if the load	has not been set yet.

>LOAD_OFF	Turn load resistor current off. This command is only valid if	a test is currently executing AND test execution is set to	manual.

>STOP_TEST	Turn off cooler relay. Turn off load resistor current. Stop	data-logging.

>SET_MANUAL_MODE	Set test execution to manual. Default value is	manual mode.
>SET_PROFILE_MODE	Set test execution to the current profile setting. This	command works, however running a profile is not	implemented yet.
>USE_PROFILE [profile]	The file given as an argument is now	selected as the profile to be executed. Verify the profile	exists. The profile file is parsed to validate it is	acceptable. Begin test execution by issuing START_TEST.
>SELFTEST	Run the built-in self test operations and report back	results. Not implemented yet.
>SET_TIME [MM-dd-YYYY]_[hh.mm.ss]	Set Pi to argument timestamp.

>SEND_LOG	upload log file(s) from the last test to the hub. This	may span more than one file if the test lasted more than one	day. Not implemented yet.
>SEND_ALL_LOGS	upload all log files stored on the flash drive to the hub	PC. If no flash drive is present, an error message is	displayed regarding missing flash drive. Not implemented.
>SET_COMPRESSOR_ID

>SET_DISPLACER_ID
>SET_DEWAR_ID
>SET_CCC_ID
>	If no argument is supplied with the Command instruction,	the list of all Commands is printed.

## Client Connection
When a client connects, the following welcome message is sent by the pi:

# Blackbox software & systemD
To configure the firmware to launch at boot, it was turned into a service launched by the systemd kernel subsystem. A file called “Blackberry.service” is located at:
/lib/systemd/system/Blackberry.service

Systemd auto-launches the executable at boot, and if the executable fails or quits for some reason, systemd will continuously attempt to relaunch the executable. This is good and verifies as long as the pi is on, we can connect to it.
One downside of the auto-launch feature is the executable doesn't launch in a terminal instance, so you can’t monitor commands and events as they happen on the pi. If you want to monitor the output on the pi you can stop the service, and launch the standalone executable. Here’s how to do it:
To stop the service:
sudo systemctl stop Blackberry.service

To restart the service:
sudo systemctl start Blackberry.service

To see the status:
sudo systemctl status Blackberry.service

To disable the service from auto-launching at boot:
sudo systemctl disable Blackberry.service

To enable the service from auto-launching at boot:
sudo systemctl enable Blackberry.service

sudo systemctl restart Blackberry.service

If for some reason the service is not working, you can view the error reporting in the following locations:
dmesg
journalctl -shows exec output for debugging
/var/log/boot.log
/var/log/daemon.log
/var/log/messages
/var/log/syslog
/var/log/user.log