PI Blackbox
Software Specification

demo software commands
May 5, 2020

Table of Contents

Table 1 - Revision History
Version	Date	Author	Changes
Draft	Jan, 27, 2020	John Polakowski	Based on group discussion of features and scope of / interface. Initial goal to provide a rapid version / of working code and conventions.

Table 2 – List of Acronyms
Acronym	Definition
DUT	Device Under Test
IDCA	Integrated Dewar Cooler Assembly
EMI	Electromagnetic Interference
PI_BB	PI Blackbox
LUT	Look Up Table

# Blackbox architecture
## Function
The Blackbox design goal is to datalog and control different metrics related to cooler testing. The Blackbox is to serve as an all-in-one piece of test equipment that can be used in many different use cases of cooler testing. These include: Lifetime Testing, Performance Testing, Burn-In Testing, …… The device under test (DUT) may be the complete IDCA, or one of its component parts (Compressor, Dewar, Displacer, CCC).

MUST EXECUTE PROGRAM WITH SUDO
## Peripherals
The peripherals of the PI_BB are:
Input Power
Power to CCC (banana plugs)
Dewar Connector (DB15)
3 thermocouples
PI USB
PI Ethernet
PI HDMI/DSI
Test Points
LEDs
## Metrics Captured
The IDCA metrics directly measured by the Pi Blackbox are:
- Power delivered to the Cooler Driver Board (Volts, mA, Watts)
- Dewar Temp Diode Voltage, and associated LUT temperature (Volts, Kelvins)
- Power delivered to heat load resistor in the Dewar (V, mA, mW)
- Heat Load State (On/Off)
- Relay State for Cooler Driver (On/Off)
- Temperature of x3 attached K-type thermocouples (Celsius)

## Capture Rate(s)
The target is to capture each metric once per second. The cooler power measurement accuracy improves considerably the more often we are able to sample it. It may become desirable at some point to reduce sampling frequency of the thermocouples, or temp diode, and increase the sampling frequency of the cooler power. For simplicity, at present all metrics are sampled equally.

The Pi firmware captures each metric sequentially, then writes the data points to file. Each datalog point of the above metrics is paired with:
- Timestamp ( MM/DD/YYYY hh:mm:ss )
- Elapsed Running Time when sample taken

# Software Specification
## Timestamp, Date-Time Naming Convention
A timestamp shall be represented in the format:
[MM-dd-YYYY]_[hh.mm.ss]

MM	2 digit month
dd	2 digit day of month
YYYY	4 digit year
hh	2 digit hour
mm	2 digit minute
ss	2 digit second

* 2 digit refers to the convention of including a leading zero if the value	is less than ten.
** To avoid AM/PM confusion, the two digit hour shall be in the 24 hour	based format. For example the hour 6:01:35 PM is represented as	18:01:35

Example:
Timestamp for Jan. 27th 2020 @ 3:18:34 PM is- 01/27/2020_15.18.34

## BlackBox Naming Convention
Each PI_BB has an associated ID. This is referred to in log files, Pi hostname, and IP address assignment. The ID scheme for a unit is as follows:
PI_BB[integer 10-240]
A valid ID would be: PI_BB20
This allocates a namespace of 230 potential blackboxes. The range of 10-240 makes sense in the IP Address space. The integer number will be the value used in the last address byte of the IP Address. The limitation to 240 follows with the largest value for an address byte: 255. The additional addresses (1-9, 241-254) are left for the hub computer, and any diagnostic PCs we might want to connect to. So for example if we have a unit named “PI_BB38”, on a network 192.168.123.0, the unit will have an IP Address of:
192.168.123.38

Additionally, the hostname for the pi will be:
pi@PI_BB38
If you open a terminal on this Pi, the resulting prompt will be:

This makes it easy to identify which Blackbox you are logged into if you SSH into the pi, or if you SCP a file to the PI.

**Possibility
If all units in a network are going to be used for a specific test, the ‘PI_BB’ could be changed to the name of the test. For instance:
pi@LifeTest20
pi@PerfTest20
pi@BurnIn20
Implementation Info
To change the hostname on a Pi two files need to be edited. These files must be edited using the ‘sudo’ command. To edit:
sudo vi /etc/hosts
sudo vi /etc/hostname
After editing and saving the above files, reboot to enable the new hostname.

Hub IP Address should always be .1
## Log File
### Log File Naming Convention:
The structure of the filename is:
BlackboxID_Date_Time.log
The specific syntax is:
PI_BB[blackbox#]_[MM-dd-YYYY]_[hh.mm.ss].log
The Date-Time timestamp is when the test begins.
All log files will end in ‘log’.
Optionally, the type of test being performed could be included in the filetype for easier file sorting in file store locations. For instance the following file extensions could be used when the type of test being performed is known:
.performance_log	Performance test log file
.lifetime_log	Lifetime Test Log files
.burnin_log	Burn-In test Log Files
.log	generic log file

Example: a log file for the performance test, which was captured using PI_BB21, and started the test on Feb. 2nd 2020 at 3:36:54 PM, would have the following log file:
PI_BB21_02-02-2020_15.36.54.performance_log
or alternatively:
PI_BB21_02-02-2020_15.36.54.log

### Log File Structure
// filename: XXXXXX
## PI_BB LOG FILE ##
firmware version XXXXX, PCB version
PI_BB: [blackbox#]
CCC:	CCC_ID
Compressor:	Compressor_ID
Dewar:	Dewar_ID
Displacer:	Displacer_ID
Test Execution:	[Manual] or [profile filename]
Test_Type:	[default/Performance/Lifetime/BurnIn]
Log Start:	[Timestamp]

[COLUMN LEGEND]
_______________________________________________________________
START	[TIMESTAMP]
DATA	[TIMESTAMP]
COMMAND	[TIMESTAMP]
DATA	[TIMESTAMP]
STOP	[TIMESTAMP]
________________________________________________________________
END

To avoid confusion and misinterpretation, the units of measure are included in both the Legend and immediately following the value of each metric.

### Log File Data Types and Format
The following are column entries in the log file. Each entry is defined as follows:
Value_ID	[data type], decimal precision*, units, example entry

CCC_V	floating point, 3, Volts, 12.432V
CCC_A	floating point, 4, Amps, 0.4328A
CCC_W	floating point, 3, Watts, 6.521W
Dewar_degK	floating point, 2, Kelvins, 117.31K
Dewar_diodeV	floating point, 3, Volts, 0.736V
Heat_Load_V	floating point, 2, Volts, 8.42V
Heat_Load_mA	floating point, 2, milliAmps, 28.31mA
Heat_Load_mW	floating point, 2, milliWatts, 100.26mW
THRMCPL_degC	floating point, 2, Celsius, 23.47C
Relay	string, [ON/OFF], state, ON
Heat_Load	string, [ON/OFF], state, OFF

*decimal precision here refers to the number of digits following the decimal point. For values less than 1, data shall have a leading 0.
For example: 0.236 = good,
.236 = not allowed
### Log File Creation and Refresh
A new log file is created, according to naming convention, at the start of test execution. A timestamp is including as part of the filename to prevent naming conflicts. The maximum length of time a log file records data is 24 hours. Whenever a new day begins ( at 00:00:00, or 12:00:00 AM), if an existing test is running, a new log file is created. The last line of the previous file instead of being “END” will be “CONTINUED” . The first line of the data section of the new file will be “PREVIOUS” instead of “START”. If the cooler is running, logging must occur.
Example:
[TODO]

### Log File Flags
START	beginning of test execution. Either manually or via profile.	Relay is closed (turned on). Metrics capture begins.
STOP	Relay is opened (turned off). Cooler turns off. May be the end	of the test or the test may continue with the cooler off.	Datalogging continues.
END	End of test. Datalogging halts. No data for this test is stored in	a subsequent timestamped file.
CONTINUED	Data for this test spans multiple files. It has data for this	test stored in a subsequent timestamped file.
PREVIOUS	Data for this test spans multiple files. It has data for this test	stored in a previously timestamped file.

The above flags are not commands, but indicators of events.
Command Instructions which are issued either from a profile or via the socket interface are echoed to the log file.
### Log File Path
If a USB drive is inserted, the Linux kernel has been configured to mount it to:
/home/pi/USB_drive/
The flash drive is the default storage device if present. The Log file path is then:
/home/pi/USB_drive/Logs/filename.log
If a USB flash drive is not detected, the micro SD card will be used to store the data, and the path will be:
/home/pi/Logs/filename.log
 DUT ID’s naming convention: TBD
- Compressor
- Dewar
- Displacer
- CCC

### Log File Upload
The Log File will be uploaded automatically when either:
- the test ends
- a new day begins, and a new file is created. Old file is uploaded
### Appending Parameters to Log File
In the future it may be desirable to annotate some derived metrics into the log file at the end of a test. These metrics might include:
- Cooldown Time
- Warmup Time
- Start Current, Stop Current
- Start Temp, Stop Temp
- Upper and Lower Bounds for power and temp, conditions when that datapoint ocurred.
## Config File
The config file stores and sets important system parameters for the PI_BB. It is not meant for regular user editing. Therefore it is a hidden file and requires elevated permissions to modify.
### Name
The config file is simply named “PI_BB.config”. Alternatively the individual blackbox number could be included, so “PI_BB38.config”. Only one config file should exist on each PI_BB.
### Config File Location
The config file is stored locally on the SD card in a hidden folder. In Linux hidden folders are named with a ‘.’ prefix. The config folder is named ‘.Config’ and is stored in the home directory.
For example:
~/.Config/PI_BB38.config
~/firmware/.config/PI_BB38.config
or
/home/pi/.Config/PI_BB38.config
/home/pi/firmware/.config/PI_BB38.config

### Config File Fields
// filename: PI_BB.config
hostname:
eth0_IP_address:
Network_address:
Subnet:
Hub_IP_address:
log file suffix (.log, .performance_log, etc)
HUB log store location
USB_flash_mount_folder:
PCB_revision_level:
Profile folder location(s)
environment variables
hostname
socket
HUB_IP_ADDR
cal file location
firmware version
## Profile File
### Profile File Structure
The file begins with a header describing the profile, the type of profile, and the profile name. After the file header is a separation line, then profile commands. For example:

// filename: XXXXX.profile
PI_BB_Profile_Definition_File
Profile_Type: [Lifetime | Performance | SADA | BurnIn | Custom]
Profile_Name: XXXXXX
Description: (description of profile)
________________________________________________________________
[COMMANDS]	[TIMESTAMPS]

### Location
Profiles to be executed are stored locally on the SD card. The profiles are stored in a folder named ‘Profiles/’ and is located in the home directory.
For example:
~/Profiles/LifetimeTest.profile
or
/home/pi/Profiles/PerformanceTest.profile

### Profile Command List

START_LOG	start data logging
RELAY_ON	close relay to power CCC
RELAY_OFF	open relay to power CCC
SET_LOAD	change load setting. Setting is in mW, default is 0.0
LOAD_ON	turn load on, adjust to setpoint
LOAD_OFF	turn load off
STOP_TEST	turn off load, turn off relay, stop logging

Each command must have an accompanying elapsed time timestamp, which indicates how much time elapses before executing the command. Every subsequent command must have a timestamp equal to or later than the previous command
Example File:
[ TODO ]
## System Startup
Once primary power is provided, the Pi begins to boot the kernel. A script is placed in the /etc/init.d/ folder which executes the following things:
- SPI and I2C enabled on the PI
- SSH enabled
- Read Config File
- Set IP Address
- Set Hostname
- Set Environment Variables
- Look for attached Flash Drive, if detected mount it
- Look for Hub to Connect to
- Sync to Network time if Available, else sync to DS3231
- Send SSH keys to hub
- Load Calibration files
- Enumerate any profiles in USB flash drive , copy to local SD card
- GPIOS are configured on the PI
- if network connected, do a package update

# parse kernel warnings
At end of test automatically upload file and unmount flash drive
log kernel errors to local non-volatile log file
# Socket Interface Specification
## Socket Instantiation
A specific port number mapping scheme needs to be decided on for the PIs and the Hub. [ TBD ]
## Socket Command Structure
All “commands” or instructions will originate from the hub computer. There are two types of instructions sent to a PI_BB:
- Get Instruction– will refer to as a ‘Query’
- Set Instruction – referred to as a ‘Command’
Query Instructions must begin with a ‘?’.
Command Instructions must begin with a ‘>’.
If an instruction is sent without the proper prefix of ‘?’ or ‘>’, or there is a typo in the instruction, the parser responds with a message:
Error: unable to parse instruction
to see command list type help
## Query List
?status	Return the following parameters:
hostname
eth0 IP address
wlan0 address
flash drive disk usage
SD card disk usage
DUT ID for:
compressor
dewar
displacer
CCC
Pi CPU temperature
Test status (whether executing a test or not)
Execution set to manual or profile
Current time & date on PI
?profiles	list the profiles currently stored on SD card
?logs	list the logs currently stored on SD card
?profile	list the current selected profile, if any
?show [filename]	print the contents of the file. Could be a profile, log, config	file,	etc.
?metrics	Returns a snapshot of the current measurements, if a test is	running. If no test is running then a message is returned:
“No Test Currently Running”
?time	Current date-time PI thinks it it right now
?	If no argument is supplied with the query instruction, the list of	query instructions is printed
help	Prints query instructions and command instructions with	usage info.
## Command List

>START_TEST	Starts test execution, within the confines of selected	test parameters. If a profile is selected, execution of the	profile begins. If test execution is set to manual, then	datalogging begins and the relay is turned on. A response is	given affirming datalogging has begun, the response	includes the name and path of the log file. Before	executing the command, the system first asks the user to	verify the test parameters. These include:
- Save Location
- Mode: manual or profile
- If profile is being run, lists the profile & run time
>RELAY_ON	Turn on the relay. This command only valid if a	test is currently executing AND test execution is set to	manual.
>RELAY_OFF	Turn off the relay. This command only valid if a	test is currently executing AND test execution is set to	manual.
>SET_LOAD	[value]	Set the load resistor setpoint. The load is not turned	on with this command, just set to the value of the supplied	argument. When the LOAD_ON command is issued, the	load disipation will at the value supplied in this command.	The units of [value] is milliWatts.This command only valid if	a test is currently executing AND test execution is set to	manual.
>LOAD_ON	Set the load resistor current to the value prescribed by the	SET_LOAD command. Default load current is 0 if the load	has not been set yet. This command is only valid if a	test is currently executing AND test execution is set to	manual.
>LOAD_OFF	Turn load resistor current off. This command is only valid if	a test is currently executing AND test execution is set to	manual.
>STOP_TEST	Turn off cooler relay. Turn off load resistor current. Stop	datalogging. Return total test execution time.
>SET_MANUAL_MODE	Set test execution to manual.

>SET_PROFILE_MODE	Set test execution to the current profile setting. If	no profile has been selected, an error is given.
>LIST_PROFILES	Display all profiles that can be found. Use ?profiles
>USE_PROFILE [profile]	The file given as an argument is now	selected as the profile to be executed. Verify the profile	exists. The profile file is parsed to validate it is	acceptable. Begin test execution by issuing START_TEST.
>SELFTEST	Run the built-in self test operations and report back	results.
>SET_TIME [MM-dd-YYYY]_[hh.mm.ss]	Set Pi to argument timestamp.

>SEND_LOG	upload log file(s) from the last test to the hub. This	may span more than one file if the test lasted more than one	day.
>SEND_ALL_LOGS	upload all log files stored on the flash drive to the hub	PC. If no flash drive is present, an error message is	displayed regarding missing flash drive.
>SET_COMPRESSOR_ID
>SET_DISPLACER_ID
>SET_DEWAR_ID
>SET_CCC_ID
>	If no argument is supplied with the Command instruction,	the list of Commands is printed.
*Note: Once profile test execution begins with the START_TEST command, all commands except for STOP_TEST are ignored.
Example Command Workflow to Run a Profile Test:

>SELFTEST	// verify PI_BB hardware is good
>USE_PROFILE [profile]	// set the profile to a specific profile file
>SET_PROFILE_MODE	// set execution to profile mode
?status	// verify test parameters look ok
>START_TEST	// run the profile

## Socket Permissions
All commands executed over the socket interface shall be executed with user account level permissions. Administrative actions require SSH login.
# PI OS Settings
## PI Relevant Folders
Logs:	/home/pi/USB_drive/Logs/	[flash drive]
/home/pi/Logs/	[ SD Card]
Profiles:	/home/pi/USB_drive/Profiles/	[flash drive]
/home/pi/Profiles/	[ SD Card]
Config:	/home/pi/.Config/	[ SD Card]
Firmware:	/home/pi/Firmware/	[ SD Card]
## SSH Keys
SSH is enabled for each PI_BB. SSH keys are generated for each Pi. At startup the PI sends the public keys to the hub for easy user level login and SCP file transfer.
## Calibration
The embedded hardware on the PI_BB PCB requires calibration to measure accurately.
[ TODO ]
## User Accounts
Two user accounts shall be created for use on the PI. One is a user level account, with permissions to do basic functions. The second account is an administrator account which can perform configuration edits, etc.
### Operator Access controlled functions
[ TODO ]
### Administrator Access Controlled functions
[ TODO ]
# Built in SELF Test function
A built in test function shall be available in the Command List. This function when exercised will perform a series of tests and report the result.
The list of information reported shall be
- CPU status
- RAM allocation for CPU and GPU
- GUI Video test
- PI_CPU temperature
- PI_USB interface up
- PI Ethernet Interface up
- Input Voltage in expected range
- Config file is filled out
- USB Flash drive detection
- Can ping Hub
- Can communicate with all onboard peripheral ICs
- Can operate relay
- temp diode and heat load resistor attached and working as expected
- Can talk to Hub over socket interface
- Real Time Clock has been set
- Synced to Network Time